## Slide 1: Applied Reinforcement Learning – Obstacle Avoidance
Alperen Gündogan
Rachid Ellouze
Uzair Akbar
Dr. Hao Shen
Hao.shen@tum.de

## Slide 2: Table of Contents
Project Objective
Completed Works
  State & Action spaces
  Approaches
  Results
Conclusion & Further Improvements

## Slide 3: Project Objectives
The turtlebot covers maximum distance within an episode.
The turtlebot avoids collisions.

## Slide 4: Time Line Review
Chart: 
| Tutorials | Implement in simulation environment | Implement in real environment | Improvments | Validate approach and final report
Start | 43587 | 43605 | 43622 | 43645 | 43658
Blue | 18 | 17 | 23 | 14 | 7
Red | 0 | 0 | 0 | 0 | 0
Green | 0 | 0 | 0 | 0 | 0
Brown | 0 | 0 | 0 | 0 | 0
Orange | 0 | 0 | 0 | 0 | 0
Purple | 0 | 0 | 0 | 0
Milestone 1 | 0 | 0.95
Milestone 2 | 0 | 0.95
Milestone 3


## Slide 5: State Space Methods
Discretize
  Grid discretizer
  VAE discretizer
Features
  Grid
  Tile coding
  Auto-Encoder
  Random

## Slide 6: Discretized Grid State Space
Joint of Lidar signals, linear velocity and angular velocity
N beams over the coverage of with resolution
Then, state space can be defined;
Where is the discretized sensor state, and are linear and angular velocities;
0.5m
1.5m
0.5m
1.5m
Discretization of LIDAR
divides the coverage into the intervals and picks the min range in that interval.
Low resolution for small ranges e.g. (0, 0.5), (0.5, 1.0).
Notes: This is the one that we exploited for the real turtlebot.
Picking the min range in an interval makes the robot more robust to noisy lidar measurements and enhance an obstacle awareness.

## Slide 7: Feature based State Spaces
TODO: Uzair

## Slide 8: Action Space
Joint of linear and angular velocities
Linear velocity: { 0.2; 0.4 m/s}
Angular velocity: { -π/6; - π/12; 0; π/12; π/6 rad/s}
Action Space
0.4m/s
0.2m/s
Linear velocity
Angular velocity
Two types;
Notes: 2 approaches for taking an action.
Combination of linear and angular velocity: 10 actions
Either change linear velocity or angular velocity: 7 actions
We used the first approach to run real turtlebot.

## Slide 9: Reward function
r
Aims of the reward function;
  Navigate as fast as possible without any collision
  Cosine term penalizes meaningless rotation

## Slide 10: Reinforcement Learning approaches
Algorithms;
  Q-Learning with eligibility traces
    Q-table
    LVFA
  SARSA with eligibility traces
    Q-table
    LVFA
Policies;
  Greedy
  Eps-greedy
  Softmax

## Slide 11: Training the agent
  Simple 2D simulator “Stage” is exploited to reduce unnecessary computational overhead.
  Apply domain randomization technique to generalize the policy during training;
Notes: We created 6 (a variety of )simulated environments with randomized properties and train a model that works across all of them.
Close the gap between simulation and reality.

## Slide 12: Improvements to run real turtlebot
  Lidar Filter
    A simple filter which observes last N consecutive lidar measurements to replace unreliable laser hits of the last measurement with the reliable ones from the previous measurements.
  Sensor Model (TODO: Uzair)
4
5
1
2
3
6
Measurements from the room -1981 to train the sensor model
Notes: To deal with the noise in the real turtlebot measurements we need to use a filter

## Slide 13: Results

## Slide 14: Demonstrations
  Simulaton
  Real world
https://youtu.be/tGrZRYJZ-YE
https://youtu.be/kJCo0gmgGCw

## Slide 15
Questions?

## Slide 16
0.5m
1.5m
0.5m
1.5m
Discretization of LIDAR
Object
Example;
State= 1, 0, 0, 0, 1, 2
BONUS